## Slide 1
01 LK_P050_07 metrics
D-L-D fusion Candidate A: 151 aa Human GLP1R B: 440 aa
Metric and scope | Value
Boltz2 Exact ipSAE (A/B, Type=max) | 0.919125
DeltaForge predicted Kd (nM) | 3.0368
Boltz2 Exact ipTM | 0.9356
Original population ipSAE rank | 1
Predicted-Kd rank within population top50 | 27
Candidate / receptor residues (aa) | 151 / 440
pDockQ / pDockQ2 | 0.3814 / 0.2607
Whole fusion / linker pLDDT (0-100) | 49.8 / 40.4
ECD / LigandForge pLDDT (0-100) | 66.6 / 40.8
Fusion design-to-refold DockQ | 0.1901
Free C-terminal OPM z (A) | 42.39
Extracellular free C-terminal screen | Pass
DeltaForge length scope | long_gt_140
Origin and prediction
ECD parent S11_02_089
LigandForge parent Design_280
Pair P050
AP Novo seed 608
Exact seed 101
3 recycles, 200 steps
ECD A1-53 linker A54-82 LF A83-151
Whole-fusion pLDDT remains modest. High interface confidence does not establish activation.
Complete selected sequence, N to C
MGISALEEFDRLRRASILLSLIRSGSTGSGFDAFLEKSGVKGAPAFLAVPSSNAFSPTSSEVAPDLPFVVLPYP
PPPSSSVIEVSGATIDLRVKTCVDFKQTVNFFKLRNTQLPGSCTKDNTVLFLLEGLKLGYASRYFSIGSGSGSQ
QFS
Human GLP1R Boltz2 Exact Computational predictions
1

## Slide 2
01 LK_P050_07 structure
D-L-D fusion Candidate A: 151 aa Human GLP1R B: 440 aa
Boltz2 Exact receptor complex
Boltz2 Exact interface detail
LigandForge
Linker
ECD binder
Receptor ECD
Remaining receptor
Hotspots
Receptor ECD B1–105 (UniProt 24–128). Black sticks: E34, Q37 and R40. View-specific zoom.
Complete selected sequence, N to C
MGISALEEFDRLRRASILLSLIRSGSTGSGFDAFLEKSGVKGAPAFLAVPSSNAFSPTSSEVAPDLPFVVLPYP
PPPSSSVIEVSGATIDLRVKTCVDFKQTVNFFKLRNTQLPGSCTKDNTVLFLLEGLKLGYASRYFSIGSGSGSQ
QFS
Human GLP1R Boltz2 Exact Computational predictions
2

## Slide 3
02 LK_P063_07 metrics
D-L-D fusion Candidate A: 140 aa Human GLP1R B: 440 aa
Metric and scope | Value
Boltz2 Exact ipSAE (A/B, Type=max) | 0.911264
DeltaForge predicted Kd (nM) | 1.3426
Boltz2 Exact ipTM | 0.8885
Original population ipSAE rank | 3
Predicted-Kd rank within population top50 | 13
Candidate / receptor residues (aa) | 140 / 440
pDockQ / pDockQ2 | 0.3717 / 0.2144
Whole fusion / linker pLDDT (0-100) | 48.6 / 43.9
ECD / LigandForge pLDDT (0-100) | 67.0 / 40.1
Fusion design-to-refold DockQ | 0.2115
Free C-terminal OPM z (A) | 60.46
Extracellular free C-terminal screen | Pass
DeltaForge length scope | platform_8_140
Origin and prediction
ECD parent S08_03_083
LigandForge parent Design_280
Pair P063
AP Novo seed 738
Exact seed 101
3 recycles, 200 steps
ECD A1-40 linker A41-71 LF A72-140
Whole-fusion pLDDT remains modest. High interface confidence does not establish activation.
Complete selected sequence, N to C
MEKKREDFKEVLKFRYSRYPSLDRFVLVNTAEESIRHLLIGMFVDPSEVLDPSPPPPPPLSLPPVPATDVVEVS
GATIDLRVKTCVDFKQTVNFFKLRNTQLPGSCTKDNTVLFLLEGLKLGYASRYFSIGSGSGSQQFS
Human GLP1R Boltz2 Exact Computational predictions
3

## Slide 4
02 LK_P063_07 structure
D-L-D fusion Candidate A: 140 aa Human GLP1R B: 440 aa
Boltz2 Exact receptor complex
Boltz2 Exact interface detail
LigandForge
Linker
ECD binder
Receptor ECD
Remaining receptor
Hotspots
Receptor ECD B1–105 (UniProt 24–128). Black sticks: E34, Q37 and R40. View-specific zoom.
Complete selected sequence, N to C
MEKKREDFKEVLKFRYSRYPSLDRFVLVNTAEESIRHLLIGMFVDPSEVLDPSPPPPPPLSLPPVPATDVVEVS
GATIDLRVKTCVDFKQTVNFFKLRNTQLPGSCTKDNTVLFLLEGLKLGYASRYFSIGSGSGSQQFS
Human GLP1R Boltz2 Exact Computational predictions
4

## Slide 5
03 LK_P109_06 metrics
D-L-D fusion Candidate A: 113 aa Human GLP1R B: 440 aa
Metric and scope | Value
Boltz2 Exact ipSAE (A/B, Type=max) | 0.910941
DeltaForge predicted Kd (nM) | 1.3294
Boltz2 Exact ipTM | 0.8713
Original population ipSAE rank | 4
Predicted-Kd rank within population top50 | 12
Candidate / receptor residues (aa) | 113 / 440
pDockQ / pDockQ2 | 0.4192 / 0.2887
Whole fusion / linker pLDDT (0-100) | 51.8 / 52.0
ECD / LigandForge pLDDT (0-100) | 78.4 / 44.1
Fusion design-to-refold DockQ | 0.2167
Free C-terminal OPM z (A) | 42.10
Extracellular free C-terminal screen | Pass
DeltaForge length scope | core_40_119
Origin and prediction
ECD parent S08_00_099
LigandForge parent Design_280
Pair P109
AP Novo seed 1197
Exact seed 101
3 recycles, 200 steps
ECD A1-20 linker A21-44 LF A45-113
Whole-fusion pLDDT remains modest. High interface confidence does not establish activation.
Complete selected sequence, N to C
MSFFQKYLKQLYLQECLSFLGGRHRVGSGSSPPPPELAPEEVVKEVSGATIDLRVKTCVDFKQTVNFFKLRNTQ
LPGSCTKDNTVLFLLEGLKLGYASRYFSIGSGSGSQQFS
Human GLP1R Boltz2 Exact Computational predictions
5

## Slide 6
03 LK_P109_06 structure
D-L-D fusion Candidate A: 113 aa Human GLP1R B: 440 aa
Boltz2 Exact receptor complex
Boltz2 Exact interface detail
LigandForge
Linker
ECD binder
Receptor ECD
Remaining receptor
Hotspots
Receptor ECD B1–105 (UniProt 24–128). Black sticks: E34, Q37 and R40. View-specific zoom.
Complete selected sequence, N to C
MSFFQKYLKQLYLQECLSFLGGRHRVGSGSSPPPPELAPEEVVKEVSGATIDLRVKTCVDFKQTVNFFKLRNTQ
LPGSCTKDNTVLFLLEGLKLGYASRYFSIGSGSGSQQFS
Human GLP1R Boltz2 Exact Computational predictions
6

## Slide 7
04 Design_520 metrics
Original LigandForge Candidate A: 53 aa Human GLP1R B: 409 aa
Metric and scope | Value
Boltz2 Exact ipSAE (A/B, Type=max) | 0.910807
DeltaForge predicted Kd (nM) | 3.4486
Boltz2 Exact ipTM | 0.9263
Original population ipSAE rank | 4
Predicted-Kd rank within population top50 | 14
Candidate / receptor residues (aa) | 53 / 409
Complex pLDDT (0-100) | 78.9
Generator-to-refold DockQ / TM-score | N/A
DeltaForge length scope | core_40_119
Origin and prediction
Original LigandForge v6.5.21
Generation 1
Exact seed 101
3 recycles, 200 steps
WT GLP1R 24-432
409 receptor residues
Original generator coordinates unavailable
Original generator coordinates are unavailable. This Exact prediction does not establish activation.
Complete selected sequence, N to C
QDVATDQGILTNVEAIFITNALYFTALLGFSDLCEARNAKKCVGSGSGSGLDR
Human GLP1R Boltz2 Exact Computational predictions
7

## Slide 8
04 Design_520 structure
Original LigandForge Candidate A: 53 aa Human GLP1R B: 409 aa
Boltz2 Exact receptor complex
Boltz2 Exact interface detail
LigandForge
Receptor ECD
Remaining receptor
Hotspots
Receptor ECD B1–105 (UniProt 24–128). Black sticks: 27 submitted pocket positions. View-specific zoom.
Complete selected sequence, N to C
QDVATDQGILTNVEAIFITNALYFTALLGFSDLCEARNAKKCVGSGSGSGLDR
Human GLP1R Boltz2 Exact Computational predictions
8

## Slide 9
05 LK_P088_08 metrics
D-L-D fusion Candidate A: 153 aa Human GLP1R B: 440 aa
Metric and scope | Value
Boltz2 Exact ipSAE (A/B, Type=max) | 0.907721
DeltaForge predicted Kd (nM) | 0.7182
Boltz2 Exact ipTM | 0.8830
Original population ipSAE rank | 5
Predicted-Kd rank within population top50 | 1
Candidate / receptor residues (aa) | 153 / 440
pDockQ / pDockQ2 | 0.2252 / 0.1339
Whole fusion / linker pLDDT (0-100) | 45.8 / 39.8
ECD / LigandForge pLDDT (0-100) | 56.6 / 40.4
Fusion design-to-refold DockQ | 0.1394
Free C-terminal OPM z (A) | 34.03
Extracellular free C-terminal screen | Pass
DeltaForge length scope | long_gt_140
Origin and prediction
ECD parent S11_03_093
LigandForge parent Design_280
Pair P088
AP Novo seed 989
Exact seed 101
3 recycles, 200 steps
LF A1-69 linker A70-101 ECD A102-153
Whole-fusion pLDDT remains modest. High interface confidence does not establish activation.
Complete selected sequence, N to C
EVSGATIDLRVKTCVDFKQTVNFFKLRNTQLPGSCTKDNTVLFLLEGLKLGYASRYFSIGSGSGSQQFSSSSST
VTRRVPPPVNLLPWGPPSGQPFPRGLGMISELQELRRLFESSYPPYFSRLLWSSYLAASVGQSDLSPTIGLGKA
LSASK
Human GLP1R Boltz2 Exact Computational predictions
9

## Slide 10
05 LK_P088_08 structure
D-L-D fusion Candidate A: 153 aa Human GLP1R B: 440 aa
Boltz2 Exact receptor complex
Boltz2 Exact interface detail
LigandForge
Linker
ECD binder
Receptor ECD
Remaining receptor
Hotspots
Receptor ECD B1–105 (UniProt 24–128). Black sticks: E34, Q37 and R40. View-specific zoom.
Complete selected sequence, N to C
EVSGATIDLRVKTCVDFKQTVNFFKLRNTQLPGSCTKDNTVLFLLEGLKLGYASRYFSIGSGSGSQQFSSSSST
VTRRVPPPVNLLPWGPPSGQPFPRGLGMISELQELRRLFESSYPPYFSRLLWSSYLAASVGQSDLSPTIGLGKA
LSASK
Human GLP1R Boltz2 Exact Computational predictions
10

## Slide 11
06 LK_P050_03 metrics
D-L-D fusion Candidate A: 149 aa Human GLP1R B: 440 aa
Metric and scope | Value
Boltz2 Exact ipSAE (A/B, Type=max) | 0.905966
DeltaForge predicted Kd (nM) | 3.2797
Boltz2 Exact ipTM | 0.9204
Original population ipSAE rank | 6
Predicted-Kd rank within population top50 | 31
Candidate / receptor residues (aa) | 149 / 440
pDockQ / pDockQ2 | 0.4071 / 0.2529
Whole fusion / linker pLDDT (0-100) | 52.0 / 41.1
ECD / LigandForge pLDDT (0-100) | 67.1 / 44.7
Fusion design-to-refold DockQ | 0.2066
Free C-terminal OPM z (A) | 38.34
Extracellular free C-terminal screen | Pass
DeltaForge length scope | long_gt_140
Origin and prediction
ECD parent S11_02_089
LigandForge parent Design_280
Pair P050
AP Novo seed 604
Exact seed 101
3 recycles, 200 steps
ECD A1-53 linker A54-80 LF A81-149
Whole-fusion pLDDT remains modest. High interface confidence does not establish activation.
Complete selected sequence, N to C
MGISALEEFDRLRRASILLSLIRSGSTGSGFDAFLEKSGVKGAPAFLAVPSSNGFDFVPSPTSSAPPLLCQGTE
PAENTREVSGATIDLRVKTCVDFKQTVNFFKLRNTQLPGSCTKDNTVLFLLEGLKLGYASRYFSIGSGSGSQQF
S
Human GLP1R Boltz2 Exact Computational predictions
11

## Slide 12
06 LK_P050_03 structure
D-L-D fusion Candidate A: 149 aa Human GLP1R B: 440 aa
Boltz2 Exact receptor complex
Boltz2 Exact interface detail
LigandForge
Linker
ECD binder
Receptor ECD
Remaining receptor
Hotspots
Receptor ECD B1–105 (UniProt 24–128). Black sticks: E34, Q37 and R40. View-specific zoom.
Complete selected sequence, N to C
MGISALEEFDRLRRASILLSLIRSGSTGSGFDAFLEKSGVKGAPAFLAVPSSNGFDFVPSPTSSAPPLLCQGTE
PAENTREVSGATIDLRVKTCVDFKQTVNFFKLRNTQLPGSCTKDNTVLFLLEGLKLGYASRYFSIGSGSGSQQF
S
Human GLP1R Boltz2 Exact Computational predictions
12

## Slide 13
07 Design_973 metrics
Original LigandForge Candidate A: 65 aa Human GLP1R B: 409 aa
Metric and scope | Value
Boltz2 Exact ipSAE (A/B, Type=max) | 0.903800
DeltaForge predicted Kd (nM) | 0.6192
Boltz2 Exact ipTM | 0.9481
Original population ipSAE rank | 8
Predicted-Kd rank within population top50 | 1
Candidate / receptor residues (aa) | 65 / 409
Complex pLDDT (0-100) | 76.8
Generator-to-refold DockQ / TM-score | N/A
DeltaForge length scope | core_40_119
Origin and prediction
Original LigandForge v6.5.21
Generation 1
Exact seed 101
3 recycles, 200 steps
WT GLP1R 24-432
409 receptor residues
Original generator coordinates unavailable
Original generator coordinates are unavailable. This Exact prediction does not establish activation.
Complete selected sequence, N to C
SKCTLHALETSFTVDPKGRFKIIAEEFSRTILGCKLLENAKFLYVVGFTEAVNLSGSGSGSPFDR
Human GLP1R Boltz2 Exact Computational predictions
13

## Slide 14
07 Design_973 structure
Original LigandForge Candidate A: 65 aa Human GLP1R B: 409 aa
Boltz2 Exact receptor complex
Boltz2 Exact interface detail
LigandForge
Receptor ECD
Remaining receptor
Hotspots
Receptor ECD B1–105 (UniProt 24–128). Black sticks: 27 submitted pocket positions. View-specific zoom.
Complete selected sequence, N to C
SKCTLHALETSFTVDPKGRFKIIAEEFSRTILGCKLLENAKFLYVVGFTEAVNLSGSGSGSPFDR
Human GLP1R Boltz2 Exact Computational predictions
14

## Slide 15
08 LK_P157_08 metrics
D-L-D fusion Candidate A: 139 aa Human GLP1R B: 440 aa
Metric and scope | Value
Boltz2 Exact ipSAE (A/B, Type=max) | 0.902451
DeltaForge predicted Kd (nM) | 3.2426
Boltz2 Exact ipTM | 0.8879
Original population ipSAE rank | 7
Predicted-Kd rank within population top50 | 30
Candidate / receptor residues (aa) | 139 / 440
pDockQ / pDockQ2 | 0.3145 / 0.1314
Whole fusion / linker pLDDT (0-100) | 54.2 / 46.3
ECD / LigandForge pLDDT (0-100) | 57.5 / 56.2
Fusion design-to-refold DockQ | 0.1548
Free C-terminal OPM z (A) | 76.82
Extracellular free C-terminal screen | Pass
DeltaForge length scope | platform_8_140
Origin and prediction
ECD parent S10_02_023
LigandForge parent Design_414
Pair P157
AP Novo seed 1679
Exact seed 101
3 recycles, 200 steps
ECD A1-50 linker A51-85 LF A86-139
Whole-fusion pLDDT remains modest. High interface confidence does not establish activation.
Complete selected sequence, N to C
MSIDYSSLVTHSPTGVAEATEFLYRYYQLREIPLETFIAVASALYHSSLLGGTDSLGKGSYDDKLNALPFSPEA
EAAAQKDVEAGKTKEGSSCVRGGSRTELFSKEPDKGVSFVSGSGVEYVCFAFFVVGSGSGSTYVS
Human GLP1R Boltz2 Exact Computational predictions
15

## Slide 16
08 LK_P157_08 structure
D-L-D fusion Candidate A: 139 aa Human GLP1R B: 440 aa
Boltz2 Exact receptor complex
Boltz2 Exact interface detail
LigandForge
Linker
ECD binder
Receptor ECD
Remaining receptor
Hotspots
Receptor ECD B1–105 (UniProt 24–128). Black sticks: E34, Q37 and R40. View-specific zoom.
Complete selected sequence, N to C
MSIDYSSLVTHSPTGVAEATEFLYRYYQLREIPLETFIAVASALYHSSLLGGTDSLGKGSYDDKLNALPFSPEA
EAAAQKDVEAGKTKEGSSCVRGGSRTELFSKEPDKGVSFVSGSGVEYVCFAFFVVGSGSGSTYVS
Human GLP1R Boltz2 Exact Computational predictions
16

## Slide 17
09 LK_P069_04 metrics
D-L-D fusion Candidate A: 154 aa Human GLP1R B: 440 aa
Metric and scope | Value
Boltz2 Exact ipSAE (A/B, Type=max) | 0.901831
DeltaForge predicted Kd (nM) | 1.2465
Boltz2 Exact ipTM | 0.8970
Original population ipSAE rank | 9
Predicted-Kd rank within population top50 | 11
Candidate / receptor residues (aa) | 154 / 440
pDockQ / pDockQ2 | 0.2443 / 0.1578
Whole fusion / linker pLDDT (0-100) | 47.1 / 40.5
ECD / LigandForge pLDDT (0-100) | 61.4 / 40.1
Fusion design-to-refold DockQ | 0.1204
Free C-terminal OPM z (A) | 48.54
Extracellular free C-terminal screen | Pass
DeltaForge length scope | long_gt_140
Origin and prediction
ECD parent S10_02_023
LigandForge parent Design_280
Pair P069
AP Novo seed 795
Exact seed 101
3 recycles, 200 steps
ECD A1-50 linker A51-85 LF A86-154
Whole-fusion pLDDT remains modest. High interface confidence does not establish activation.
Complete selected sequence, N to C
MSIDYSSLVTHSPTGVAEATEFLYRYYQLREIPLETFIAVASALYHSSLLGGLGEFSDNGLPPVAPLPPGLPVP
DLPQDEESDIKEVSGATIDLRVKTCVDFKQTVNFFKLRNTQLPGSCTKDNTVLFLLEGLKLGYASRYFSIGSGS
GSQQFS
Human GLP1R Boltz2 Exact Computational predictions
17

## Slide 18
09 LK_P069_04 structure
D-L-D fusion Candidate A: 154 aa Human GLP1R B: 440 aa
Boltz2 Exact receptor complex
Boltz2 Exact interface detail
LigandForge
Linker
ECD binder
Receptor ECD
Remaining receptor
Hotspots
Receptor ECD B1–105 (UniProt 24–128). Black sticks: E34, Q37 and R40. View-specific zoom.
Complete selected sequence, N to C
MSIDYSSLVTHSPTGVAEATEFLYRYYQLREIPLETFIAVASALYHSSLLGGLGEFSDNGLPPVAPLPPGLPVP
DLPQDEESDIKEVSGATIDLRVKTCVDFKQTVNFFKLRNTQLPGSCTKDNTVLFLLEGLKLGYASRYFSIGSGS
GSQQFS
Human GLP1R Boltz2 Exact Computational predictions
18

## Slide 19
10 LK_P024_03 metrics
D-L-D fusion Candidate A: 128 aa Human GLP1R B: 440 aa
Metric and scope | Value
Boltz2 Exact ipSAE (A/B, Type=max) | 0.901677
DeltaForge predicted Kd (nM) | 3.7889
Boltz2 Exact ipTM | 0.8706
Original population ipSAE rank | 10
Predicted-Kd rank within population top50 | 33
Candidate / receptor residues (aa) | 128 / 440
pDockQ / pDockQ2 | 0.3381 / 0.2317
Whole fusion / linker pLDDT (0-100) | 57.3 / 51.5
ECD / LigandForge pLDDT (0-100) | 69.3 / 49.8
Fusion design-to-refold DockQ | 0.2143
Free C-terminal OPM z (A) | 39.32
Extracellular free C-terminal screen | Pass
DeltaForge length scope | platform_8_140
Origin and prediction
ECD parent S11_00_040
LigandForge parent Design_613
Pair P024
AP Novo seed 344
Exact seed 101
3 recycles, 200 steps
ECD A1-48 linker A49-66 LF A67-128
Whole-fusion pLDDT remains modest. High interface confidence does not establish activation.
Complete selected sequence, N to C
MRALAQASTGSSALETLHRMRVEAFFQQQLRSGTLSDGAVEAYSRLVGGGHRVEPPVRPPPVSLPGRTCTSAYG
VPYSDGHFQRPVPSENGLNTQGVTDVSGRETDESTDVFVVISCQGSGSGSTRFN
Human GLP1R Boltz2 Exact Computational predictions
19

## Slide 20
10 LK_P024_03 structure
D-L-D fusion Candidate A: 128 aa Human GLP1R B: 440 aa
Boltz2 Exact receptor complex
Boltz2 Exact interface detail
LigandForge
Linker
ECD binder
Receptor ECD
Remaining receptor
Hotspots
Receptor ECD B1–105 (UniProt 24–128). Black sticks: E34, Q37 and R40. View-specific zoom.
Complete selected sequence, N to C
MRALAQASTGSSALETLHRMRVEAFFQQQLRSGTLSDGAVEAYSRLVGGGHRVEPPVRPPPVSLPGRTCTSAYG
VPYSDGHFQRPVPSENGLNTQGVTDVSGRETDESTDVFVVISCQGSGSGSTRFN
Human GLP1R Boltz2 Exact Computational predictions
20

## Slide 21
11 Design_994 metrics
Original LigandForge Candidate A: 70 aa Human GLP1R B: 409 aa
Metric and scope | Value
Boltz2 Exact ipSAE (A/B, Type=max) | 0.900959
DeltaForge predicted Kd (nM) | 2.7380
Boltz2 Exact ipTM | 0.9553
Original population ipSAE rank | 11
Predicted-Kd rank within population top50 | 12
Candidate / receptor residues (aa) | 70 / 409
Complex pLDDT (0-100) | 74.4
Generator-to-refold DockQ / TM-score | N/A
DeltaForge length scope | core_40_119
Origin and prediction
Original LigandForge v6.5.21
Generation 1
Exact seed 101
3 recycles, 200 steps
WT GLP1R 24-432
409 receptor residues
Original generator coordinates unavailable
Original generator coordinates are unavailable. This Exact prediction does not establish activation.
Complete selected sequence, N to C
TIDGYKHLFEISDVIEAEGGELQLKRQEYESAIGFKLCRLNAESVYNVKKLSGLRPVGCKGSGSGSYVNL
Human GLP1R Boltz2 Exact Computational predictions
21

## Slide 22
11 Design_994 structure
Original LigandForge Candidate A: 70 aa Human GLP1R B: 409 aa
Boltz2 Exact receptor complex
Boltz2 Exact interface detail
LigandForge
Receptor ECD
Remaining receptor
Hotspots
Receptor ECD B1–105 (UniProt 24–128). Black sticks: 27 submitted pocket positions. View-specific zoom.
Complete selected sequence, N to C
TIDGYKHLFEISDVIEAEGGELQLKRQEYESAIGFKLCRLNAESVYNVKKLSGLRPVGCKGSGSGSYVNL
Human GLP1R Boltz2 Exact Computational predictions
22

## Slide 23
12 LK_P012_08 metrics
D-L-D fusion Candidate A: 125 aa Human GLP1R B: 440 aa
Metric and scope | Value
Boltz2 Exact ipSAE (A/B, Type=max) | 0.900529
DeltaForge predicted Kd (nM) | 1.4449
Boltz2 Exact ipTM | 0.9175
Original population ipSAE rank | 11
Predicted-Kd rank within population top50 | 14
Candidate / receptor residues (aa) | 125 / 440
pDockQ / pDockQ2 | 0.2348 / 0.1121
Whole fusion / linker pLDDT (0-100) | 47.9 / 41.6
ECD / LigandForge pLDDT (0-100) | 67.4 / 38.2
Fusion design-to-refold DockQ | 0.2160
Free C-terminal OPM z (A) | 34.03
Extracellular free C-terminal screen | Pass
DeltaForge length scope | platform_8_140
Origin and prediction
ECD parent S08_00_042
LigandForge parent Design_991
Pair P012
AP Novo seed 229
Exact seed 101
3 recycles, 200 steps
ECD A1-39 linker A40-60 LF A61-125
Whole-fusion pLDDT remains modest. High interface confidence does not establish activation.
Complete selected sequence, N to C
MADSISEVSEGVHLILAAQALELPPFVVAARLEEARAKRGGAPSFLPPPNVTSGYVNGGGAFHLTGLAARCGAV
WRGVFCQFGNGVKGEGSVTGGSLNTFYILTVAPTSANILTSGSGSGSLEGS
Human GLP1R Boltz2 Exact Computational predictions
23

## Slide 24
12 LK_P012_08 structure
D-L-D fusion Candidate A: 125 aa Human GLP1R B: 440 aa
Boltz2 Exact receptor complex
Boltz2 Exact interface detail
LigandForge
Linker
ECD binder
Receptor ECD
Remaining receptor
Hotspots
Receptor ECD B1–105 (UniProt 24–128). Black sticks: E34, Q37 and R40. View-specific zoom.
Complete selected sequence, N to C
MADSISEVSEGVHLILAAQALELPPFVVAARLEEARAKRGGAPSFLPPPNVTSGYVNGGGAFHLTGLAARCGAV
WRGVFCQFGNGVKGEGSVTGGSLNTFYILTVAPTSANILTSGSGSGSLEGS
Human GLP1R Boltz2 Exact Computational predictions
24

## Slide 25
13 LK_P062_00 metrics
D-L-D fusion Candidate A: 146 aa Human GLP1R B: 440 aa
Metric and scope | Value
Boltz2 Exact ipSAE (A/B, Type=max) | 0.900237
DeltaForge predicted Kd (nM) | 1.1314
Boltz2 Exact ipTM | 0.8780
Original population ipSAE rank | 12
Predicted-Kd rank within population top50 | 10
Candidate / receptor residues (aa) | 146 / 440
pDockQ / pDockQ2 | 0.2581 / 0.1250
Whole fusion / linker pLDDT (0-100) | 55.9 / 49.4
ECD / LigandForge pLDDT (0-100) | 61.5 / 55.0
Fusion design-to-refold DockQ | 0.1047
Free C-terminal OPM z (A) | 49.68
Extracellular free C-terminal screen | Pass
DeltaForge length scope | long_gt_140
Origin and prediction
ECD parent S10_04_045
LigandForge parent Design_280
Pair P062
AP Novo seed 721
Exact seed 101
3 recycles, 200 steps
ECD A1-46 linker A47-77 LF A78-146
Whole-fusion pLDDT remains modest. High interface confidence does not establish activation.
Complete selected sequence, N to C
MTDIGEEIKALVALTEGVPPENRPFAVELAQRLSPWFSLYSRLSSRGGVGSGHPLEPITIVRPPPVPELEPITG
PVTEVSGATIDLRVKTCVDFKQTVNFFKLRNTQLPGSCTKDNTVLFLLEGLKLGYASRYFSIGSGSGSQQFS
Human GLP1R Boltz2 Exact Computational predictions
25

## Slide 26
13 LK_P062_00 structure
D-L-D fusion Candidate A: 146 aa Human GLP1R B: 440 aa
Boltz2 Exact receptor complex
Boltz2 Exact interface detail
LigandForge
Linker
ECD binder
Receptor ECD
Remaining receptor
Hotspots
Receptor ECD B1–105 (UniProt 24–128). Black sticks: E34, Q37 and R40. View-specific zoom.
Complete selected sequence, N to C
MTDIGEEIKALVALTEGVPPENRPFAVELAQRLSPWFSLYSRLSSRGGVGSGHPLEPITIVRPPPVPELEPITG
PVTEVSGATIDLRVKTCVDFKQTVNFFKLRNTQLPGSCTKDNTVLFLLEGLKLGYASRYFSIGSGSGSQQFS
Human GLP1R Boltz2 Exact Computational predictions
26

## Slide 27
14 Design_440 metrics
Original LigandForge Candidate A: 54 aa Human GLP1R B: 409 aa
Metric and scope | Value
Boltz2 Exact ipSAE (A/B, Type=max) | 0.900081
DeltaForge predicted Kd (nM) | 4.3955
Boltz2 Exact ipTM | 0.9633
Original population ipSAE rank | 13
Predicted-Kd rank within population top50 | 19
Candidate / receptor residues (aa) | 54 / 409
Complex pLDDT (0-100) | 79.0
Generator-to-refold DockQ / TM-score | N/A
DeltaForge length scope | core_40_119
Origin and prediction
Original LigandForge v6.5.21
Generation 1
Exact seed 101
3 recycles, 200 steps
WT GLP1R 24-432
409 receptor residues
Original generator coordinates unavailable
Original generator coordinates are unavailable. This Exact prediction does not establish activation.
Complete selected sequence, N to C
PNYFGFTGFLCIVGDINIGRKAEEFQFFGAIKGGGIEFVCKSDVGSGSGSILFN
Human GLP1R Boltz2 Exact Computational predictions
27

## Slide 28
14 Design_440 structure
Original LigandForge Candidate A: 54 aa Human GLP1R B: 409 aa
Boltz2 Exact receptor complex
Boltz2 Exact interface detail
LigandForge
Receptor ECD
Remaining receptor
Hotspots
Receptor ECD B1–105 (UniProt 24–128). Black sticks: 27 submitted pocket positions. View-specific zoom.
Complete selected sequence, N to C
PNYFGFTGFLCIVGDINIGRKAEEFQFFGAIKGGGIEFVCKSDVGSGSGSILFN
Human GLP1R Boltz2 Exact Computational predictions
28

## Slide 29
15 LK_P141_07 metrics
D-L-D fusion Candidate A: 121 aa Human GLP1R B: 440 aa
Metric and scope | Value
Boltz2 Exact ipSAE (A/B, Type=max) | 0.899774
DeltaForge predicted Kd (nM) | 1.6270
Boltz2 Exact ipTM | 0.8838
Original population ipSAE rank | 14
Predicted-Kd rank within population top50 | 17
Candidate / receptor residues (aa) | 121 / 440
pDockQ / pDockQ2 | 0.4125 / 0.2650
Whole fusion / linker pLDDT (0-100) | 59.9 / 61.7
ECD / LigandForge pLDDT (0-100) | 71.4 / 54.1
Fusion design-to-refold DockQ | 0.2736
Free C-terminal OPM z (A) | 76.38
Extracellular free C-terminal screen | Pass
DeltaForge length scope | platform_8_140
Origin and prediction
ECD parent S09_03_086
LigandForge parent Design_280
Pair P141
AP Novo seed 1518
Exact seed 101
3 recycles, 200 steps
ECD A1-32 linker A33-52 LF A53-121
Whole-fusion pLDDT remains modest. High interface confidence does not establish activation.
Complete selected sequence, N to C
MVSIGSTGFDGLLQLDEELRNLFLQRLVLGRLGSGLPPPPPPVDVIPPSEVKEVSGATIDLRVKTCVDFKQTVN
FFKLRNTQLPGSCTKDNTVLFLLEGLKLGYASRYFSIGSGSGSQQFS
Human GLP1R Boltz2 Exact Computational predictions
29

## Slide 30
15 LK_P141_07 structure
D-L-D fusion Candidate A: 121 aa Human GLP1R B: 440 aa
Boltz2 Exact receptor complex
Boltz2 Exact interface detail
LigandForge
Linker
ECD binder
Receptor ECD
Remaining receptor
Hotspots
Receptor ECD B1–105 (UniProt 24–128). Black sticks: E34, Q37 and R40. View-specific zoom.
Complete selected sequence, N to C
MVSIGSTGFDGLLQLDEELRNLFLQRLVLGRLGSGLPPPPPPVDVIPPSEVKEVSGATIDLRVKTCVDFKQTVN
FFKLRNTQLPGSCTKDNTVLFLLEGLKLGYASRYFSIGSGSGSQQFS
Human GLP1R Boltz2 Exact Computational predictions
30

## Slide 31
16 LK_P002_05 metrics
D-L-D fusion Candidate A: 104 aa Human GLP1R B: 440 aa
Metric and scope | Value
Boltz2 Exact ipSAE (A/B, Type=max) | 0.899462
DeltaForge predicted Kd (nM) | 0.8130
Boltz2 Exact ipTM | 0.9370
Original population ipSAE rank | 16
Predicted-Kd rank within population top50 | 4
Candidate / receptor residues (aa) | 104 / 440
pDockQ / pDockQ2 | 0.1832 / 0.1014
Whole fusion / linker pLDDT (0-100) | 43.8 / 38.2
ECD / LigandForge pLDDT (0-100) | 51.5 / 37.1
Fusion design-to-refold DockQ | 0.0893
Free C-terminal OPM z (A) | 42.07
Extracellular free C-terminal screen | Pass
DeltaForge length scope | core_40_119
Origin and prediction
ECD parent S10_03_014
LigandForge parent Design_913
Pair P002
AP Novo seed 126
Exact seed 101
3 recycles, 200 steps
LF A1-36 linker A37-57 ECD A58-104
Whole-fusion pLDDT remains modest. High interface confidence does not establish activation.
Complete selected sequence, N to C
NLPRIECSSNKGNVQEDSDVIGGRGSGSGSGSCGIFGKTSTSGPQPVIILPVPVLPGMLPQLFLTHMLSVMVGT
GSLDSGLVSAFRGSPLVSEAILGFLKQYLS
Human GLP1R Boltz2 Exact Computational predictions
31

## Slide 32
16 LK_P002_05 structure
D-L-D fusion Candidate A: 104 aa Human GLP1R B: 440 aa
Boltz2 Exact receptor complex
Boltz2 Exact interface detail
LigandForge
Linker
ECD binder
Receptor ECD
Remaining receptor
Hotspots
Receptor ECD B1–105 (UniProt 24–128). Black sticks: E34, Q37 and R40. View-specific zoom.
Complete selected sequence, N to C
NLPRIECSSNKGNVQEDSDVIGGRGSGSGSGSCGIFGKTSTSGPQPVIILPVPVLPGMLPQLFLTHMLSVMVGT
GSLDSGLVSAFRGSPLVSEAILGFLKQYLS
Human GLP1R Boltz2 Exact Computational predictions
32

## Slide 33
17 LK_P012_04 metrics
D-L-D fusion Candidate A: 130 aa Human GLP1R B: 440 aa
Metric and scope | Value
Boltz2 Exact ipSAE (A/B, Type=max) | 0.899333
DeltaForge predicted Kd (nM) | 2.1528
Boltz2 Exact ipTM | 0.8851
Original population ipSAE rank | 17
Predicted-Kd rank within population top50 | 22
Candidate / receptor residues (aa) | 130 / 440
pDockQ / pDockQ2 | 0.2455 / 0.1128
Whole fusion / linker pLDDT (0-100) | 46.2 / 36.0
ECD / LigandForge pLDDT (0-100) | 70.6 / 35.7
Fusion design-to-refold DockQ | 0.2180
Free C-terminal OPM z (A) | 33.84
Extracellular free C-terminal screen | Pass
DeltaForge length scope | platform_8_140
Origin and prediction
ECD parent S08_00_042
LigandForge parent Design_991
Pair P012
AP Novo seed 225
Exact seed 101
3 recycles, 200 steps
ECD A1-39 linker A40-65 LF A66-130
Whole-fusion pLDDT remains modest. High interface confidence does not establish activation.
Complete selected sequence, N to C
MADSISEVSEGVHLILAAQALELPPFVVAARLEEARAKRPGSSLLPLPEDTSDVASGSISYPGASAFHLTGLAA
RCGAVWRGVFCQFGNGVKGEGSVTGGSLNTFYILTVAPTSANILTSGSGSGSLEGS
Human GLP1R Boltz2 Exact Computational predictions
33

## Slide 34
17 LK_P012_04 structure
D-L-D fusion Candidate A: 130 aa Human GLP1R B: 440 aa
Boltz2 Exact receptor complex
Boltz2 Exact interface detail
LigandForge
Linker
ECD binder
Receptor ECD
Remaining receptor
Hotspots
Receptor ECD B1–105 (UniProt 24–128). Black sticks: E34, Q37 and R40. View-specific zoom.
Complete selected sequence, N to C
MADSISEVSEGVHLILAAQALELPPFVVAARLEEARAKRPGSSLLPLPEDTSDVASGSISYPGASAFHLTGLAA
RCGAVWRGVFCQFGNGVKGEGSVTGGSLNTFYILTVAPTSANILTSGSGSGSLEGS
Human GLP1R Boltz2 Exact Computational predictions
34

## Slide 35
18 Design_787 metrics
Original LigandForge Candidate A: 49 aa Human GLP1R B: 409 aa
Metric and scope | Value
Boltz2 Exact ipSAE (A/B, Type=max) | 0.899274
DeltaForge predicted Kd (nM) | 5.3824
Boltz2 Exact ipTM | 0.9546
Original population ipSAE rank | 14
Predicted-Kd rank within population top50 | 20
Candidate / receptor residues (aa) | 49 / 409
Complex pLDDT (0-100) | 78.6
Generator-to-refold DockQ / TM-score | N/A
DeltaForge length scope | core_40_119
Origin and prediction
Original LigandForge v6.5.21
Generation 1
Exact seed 101
3 recycles, 200 steps
WT GLP1R 24-432
409 receptor residues
Original generator coordinates unavailable
Original generator coordinates are unavailable. This Exact prediction does not establish activation.
Complete selected sequence, N to C
GTLALTHCVFAADRAEIFGQRGKEDLQTGKAASEGTELTGSGSGSLCDI
Human GLP1R Boltz2 Exact Computational predictions
35

## Slide 36
18 Design_787 structure
Original LigandForge Candidate A: 49 aa Human GLP1R B: 409 aa
Boltz2 Exact receptor complex
Boltz2 Exact interface detail
LigandForge
Receptor ECD
Remaining receptor
Hotspots
Receptor ECD B1–105 (UniProt 24–128). Black sticks: 27 submitted pocket positions. View-specific zoom.
Complete selected sequence, N to C
GTLALTHCVFAADRAEIFGQRGKEDLQTGKAASEGTELTGSGSGSLCDI
Human GLP1R Boltz2 Exact Computational predictions
36

## Slide 37
19 Design_15 metrics
Original LigandForge Candidate A: 50 aa Human GLP1R B: 409 aa
Metric and scope | Value
Boltz2 Exact ipSAE (A/B, Type=max) | 0.898565
DeltaForge predicted Kd (nM) | 4.2907
Boltz2 Exact ipTM | 0.9471
Original population ipSAE rank | 15
Predicted-Kd rank within population top50 | 18
Candidate / receptor residues (aa) | 50 / 409
Complex pLDDT (0-100) | 69.4
Generator-to-refold DockQ / TM-score | N/A
DeltaForge length scope | core_40_119
Origin and prediction
Original LigandForge v6.5.21
Generation 1
Exact seed 101
3 recycles, 200 steps
WT GLP1R 24-432
409 receptor residues
Original generator coordinates unavailable
Original generator coordinates are unavailable. This Exact prediction does not establish activation.
Complete selected sequence, N to C
AQCTKTYAIGYDVYLKLTYLGFRRADGAGNDDDVCAGNVGGSGSGSFFVA
Human GLP1R Boltz2 Exact Computational predictions
37

## Slide 38
19 Design_15 structure
Original LigandForge Candidate A: 50 aa Human GLP1R B: 409 aa
Boltz2 Exact receptor complex
Boltz2 Exact interface detail
LigandForge
Receptor ECD
Remaining receptor
Hotspots
Receptor ECD B1–105 (UniProt 24–128). Black sticks: 27 submitted pocket positions. View-specific zoom.
Complete selected sequence, N to C
AQCTKTYAIGYDVYLKLTYLGFRRADGAGNDDDVCAGNVGGSGSGSFFVA
Human GLP1R Boltz2 Exact Computational predictions
38

## Slide 39
20 LK_P093_03 metrics
D-L-D fusion Candidate A: 159 aa Human GLP1R B: 440 aa
Metric and scope | Value
Boltz2 Exact ipSAE (A/B, Type=max) | 0.898297
DeltaForge predicted Kd (nM) | 0.8232
Boltz2 Exact ipTM | 0.8864
Original population ipSAE rank | 19
Predicted-Kd rank within population top50 | 5
Candidate / receptor residues (aa) | 159 / 440
pDockQ / pDockQ2 | 0.4014 / 0.1735
Whole fusion / linker pLDDT (0-100) | 52.4 / 42.3
ECD / LigandForge pLDDT (0-100) | 68.2 / 43.1
Fusion design-to-refold DockQ | 0.2733
Free C-terminal OPM z (A) | 63.98
Extracellular free C-terminal screen | Pass
DeltaForge length scope | long_gt_140
Origin and prediction
ECD parent S10_02_067
LigandForge parent Design_280
Pair P093
AP Novo seed 1034
Exact seed 101
3 recycles, 200 steps
ECD A1-60 linker A61-90 LF A91-159
Whole-fusion pLDDT remains modest. High interface confidence does not establish activation.
Complete selected sequence, N to C
SSSSSVPAPSIDYLGAFREHGANAEVAEFLYRYLREIKGKSEKEAILLLTAAASIANLVAGISSSVPDPRTPPP
PPPPVPVEPLDPSSLTEVSGATIDLRVKTCVDFKQTVNFFKLRNTQLPGSCTKDNTVLFLLEGLKLGYASRYFS
IGSGSGSQQFS
Human GLP1R Boltz2 Exact Computational predictions
39

## Slide 40
20 LK_P093_03 structure
D-L-D fusion Candidate A: 159 aa Human GLP1R B: 440 aa
Boltz2 Exact receptor complex
Boltz2 Exact interface detail
LigandForge
Linker
ECD binder
Receptor ECD
Remaining receptor
Hotspots
Receptor ECD B1–105 (UniProt 24–128). Black sticks: E34, Q37 and R40. View-specific zoom.
Complete selected sequence, N to C
SSSSSVPAPSIDYLGAFREHGANAEVAEFLYRYLREIKGKSEKEAILLLTAAASIANLVAGISSSVPDPRTPPP
PPPPVPVEPLDPSSLTEVSGATIDLRVKTCVDFKQTVNFFKLRNTQLPGSCTKDNTVLFLLEGLKLGYASRYFS
IGSGSGSQQFS
Human GLP1R Boltz2 Exact Computational predictions
40